## Slide 1
Magnus Rydén
Chalmers University of Technology
Email: magnus.ryden@chalmers.se
Cutting the cost for biogenic CO2
– the principles and development status of Chemical-Looping Combustion (CLC) of biomass
Expanding Horizons in the Hydrogen Economy: Integrating Energy, Material Production, and CCU Value Chains - Insight Harvest
2024-10-16
Notes: To add text in the slide master:
Go to the top menu, choose > View > Slide Master. In the absolute first slide, change to the preferred text.
Close Master View. The new text will permeate on all slides.

## Slide 2: Content
The case for Chemical-Looping Combustion.
ACLOUD project pitch and activities.
CLC current status and future research needs.

## Slide 3: Chemical-Looping Combustion (CLC)
OC-O(s)
Fuel reactor: CH4 + 12Fe2O3(s) → CO2 + 2 H2O + 8Fe3O4(s)
Air reactor: 2 O2 + 8 Fe3O4(s) → 12Fe2O3(s)
Total reaction: CH4 + 2 O2 → CO2 + 2 H2O
OC(s)
Air
O2, N2
Fuel
Flue gas
CO2, H2O
Nitrogen
N2
Air Reactor
Fuel reactor
Example
Fuel = CH4
OC-O = Fe2O3
OC = Fe3O4
Heat

## Slide 4: Basic reactor design
Air
Depleted air
Fuel
Products
Air reactor
Cyclone
Fuel reactor
Seals
Sand-like particles of oxygen-carrier material (0.1-0.4 mm) as bed material.
High gas velocity (2-5 m/s) in the air reactor which acts as riser, particles are blown upwards and into a cyclone.
The particles are transported by gravity to the fuel reactor in which they are reduced by fuel, then continues to the air reactor.
Gas leakage between the reactors is prevented by fluidized particle seals.
Typically, near atmospheric pressure and temperature 800-1050°C.
Many variations has been proposed and tested. Still, the basic setup serves its purpose well.

## Slide 5: Circulating Fluidized Bed boiler (CFB)
Air
Fuel
Products
Air reactor
Cyclone
Fuel reactor
Seals

## Slide 6: Circulating Fluidized Bed boiler (CFB)
Air
Fuel
Products
Air reactor
Cyclone
Fuel reactor
Seals
Air reactor
Fuel reactor

## Slide 7
CLC can reduce the energy penalty for CO2 capture. In theory, there is no energy penalty compared to conventional combustion.
CLC can have close to 100% capture rate without extra costs or efforts.
Compared to post combustion, CLC has low CAPEX and small footprint. Everything can fit within the confined walls of a CFB boiler.
CLC does not require harmful chemicals. The oxygen carrier can be mineral ores (e.g. ilmenite) or slag products from mineral industries.
CLC has potential to reduce CO2 capture cost for several applications. For solid fuel combustion, most studies suggests ≈20 euro/tonCO2.
Why even bother with CLC?

## Slide 8: ACLOUD Project Pitch
In northern Europe, biomass and forestry waste are important domestic fuels.
In Europe as a whole, the use of waste-derived fuels seems destined to increase.
Difficult to convert, being inhomogeneous and rich in problematic ash species.
CLC could be an ideal conversion technology for difficult fuels. It provides inherent CO2 capture, O2 buffering to counter inhomogeneity and also separates heat-transfer surfaces from ash.

## Slide 9: ACLOUD Project Pitch
No or minimal ash species
Atmosphere mainly N2 and O2
Temperature 900-1050°C
Air factor can be reduced
≈100% of heat generation
≈70% of total gas flow
Minimal ash and deposits
Slightly reduced heat flow
Reduced gas radiation
Atmosphere mainly CO2 and H2O
Concentrated ash and impurities
Temperature 900-1050°C
≈Adiabatic reactor
≈30% of total gas flow
CFB, dual-CFB or other design?
Separate convection path?
Flue gas conditioning?
Air reactor
Fuel reactor
No aggressive ash species here means that steam data can be increased, which means electric efficiency could be improved.

## Slide 10: Project Activities
Demonstration at 1 MW scale with at least two relevant domestic fuels.
Work on pilot and lab scale related to fuel conversion pathways and ash chemistry. This includes development of new analysis and measurement techniques.
Corrosion and material studies, including applied on 1 MW and 10 kW pilot reactors.
Economic performance and environmental impact for key applications, such as e.g. waste-to-energy and combined heat-power.

## Slide 11: Current status of CLC
Demonstrated in >>50 different pilot reactors for in total >>12000 h, using all sorts of fuels and a huge range of oxygen carriers. ≈80% of global experience is in Europe.
Demonstrated up to 5 MWth scale, but most work is at 0.1-100 kWth.
100% fuel conversion and 100% CO2 capture feasible with gaseous fuels.
With coal and biomass >>90% fuel conversion and >>90% CO2 capture is a realistic target. However, it is clear that dedicated flue gas conditioning and cleaning needs to be designed and developed.
The use and logistics of oxygen carriers have been demonstrated in >12 full-scale boilers in Sweden by Eon/Improbed, but without CO2 capture.

## Slide 12: Logotype